## Slide 1
UCL Interfaces

## Slide 2: UCL interfaces
Task Id: TFDCX32348-26059, DICMBD-47
UCL Interface (Leveraged from Hyundai):
Showing a warning in Display
UclWarningDisplayMsg
Description: Display / hide warning with dynamic data
Timing: On change with a periodicity of 30ms
Arguments : show(uint8) , warningId(uint16), dynData(uint8[6]);
Show : Tells whether to display or not display the warning . Hide(0), Show (1), StoreHide(2)
warningId : Current warning ID (ensure the id < Total number of available warnings)
dynData : Payload data

## Slide 3: UCL interfaces
UCL Interface(Leveraged from Hyundai):
Feedback from HMI i.e. Displayed status of the warning :
UclWarningStatusMsg
Warning that is being displayed
Timing: On write with a with a periodicity of 30ms
Arguments : visible(uint8) , warningId(uint16), dynData(uint8[8]);
visible : Tells whether the warning is in display or not. 0 - Not Visible, 1 - Visible
warningId : Current warning ID (ensure the id < Total number of available warnings)
dynData : Payload data. i.e. Acknowledged, button handling.
Task Id: TFDCX32348-26059, DICMBD-47

## Slide 4: UCL interfaces
UCL Interface(Leveraged from Hyundai):
Stored Warning:
UclInfoTabData
Stored Warning data that needs to be displayed
Timing: On change Arguments : InfoWarningCount (uint8) , InfoWarningList(SInfoWarningList_t[89]), dynData(uint8[8]);
InfoWarningCount : Tells current number of active Stored warnings
InfoWarningList : ID of the stored warning and its payload
SInfoWarningList : WarningID
WarningPayload
dynData : (If needed)
This message is program specific and will be finalized if post concurrence with HMI.
Task Id: TFDCX32348-26059, DICMBD-47

## Slide 5: UCL interfaces - HLD
Interface:
The following component needs to be added in SWC – CWarnMsg_Core_Observer and CWarnMsgCore_TmrSupport
S.No | Interface | Type | Short Description | Provider/Receiver
1 | Rte_Write_CWarnMsg_Core_Observer_WarningDisplayData | Sender-Receiver | This write port sends the data of the warning to be displayed to HMI via UCL | UCL Adapter (R)
2 | OnDre_UCL_WarnStatus | Client-Server | Invoked by Rte_NonTrusted on Acknowledgement to a warning | CWarnMsg_Core_Observer
3 | Rte_Send_CWarnMsg_Core_Observer_ppStoredWrnStsUCL_StoreWarningData | Sender-Receiver | This sends the stored warning data to the HMI | CWarnMsg_Core_Observer
4 | Rte_Read_CWarnMsg_Core_Observer_rpWarnStatus_WarningStatusData | Sender-Receiver | This read port receives the data of the warning displayed from HMI via UCL | UCL Adapter (P)
Task Id: TFDCX32348-26059, DICMBD-47