## Slide 1
Update Warning Status – Pros and Cons

## Slide 2: Pros and cons of using UpdateWarningStatus
Task Id: TFDCX32348-26058
Proceeding with the current interface that has the payload as that is the Platform Interface as per Hyundai UCL catalogue.
Pros :
1. The setting/clearing of warnings, the event type and payload can be conveyed in a single interface.
2. Single RTE across all waring components leads to less conflicts.
3. Single array in the Control warning side leading to easy readability for HMI and also for debugging purpose.
4. No multiple interfaces for clearing, setting with event and payload data.
Cons:
1. Warnings that have no payload or event will pass those arguments with invalid data.
2. The payload size is currently limited to 32bit, any additional data beyond this will need a separate interface.
3. The Payload is not used currently in Toyota and hence 2KB of memory is unnecessarily occupied. Hence payload argument can to be removed.